## Slide 1
Varendra University
Dept. of Computer Science & Engineering (CSE)
Lab 1
Course Title: Microprocessor and Assembly Language Lab
Course No: CSE 3206
Prepared By:
Md. Adnan Sami
Lecturer, Dept. of CSE, VU

## Slide 3
Register:
  Data Register
    AX (Accumulator Register)
    BX (Base Register)
    CX (Count Register)
    DX (Data Register)
  AX = AH AL
  BX = BH BL
  CX = CH CL
  DX = DH DL

## Slide 4
  AX = AH AL
  BX = BH BL
  CX = CH CL
  DX = DH DL
  AL is reserved for input.
  DL is reserved for output.

## Slide 5
  MOV AH, 1
  Operand
  Opcode
  Opcode: Operation.
  Operand: 2 parts,
          Destination.
          Source.

## Slide 6
  Opcode Destination, Source
  MOV AH, 1
  Destination
  Source
  Destination: The register or memory location where data is stored.
  Source: Provides the data.
  MOV: Used to transfer data from one location to another.

## Slide 7
  For Input:
    mov ah,1
    int 21h
    mov bl,al
  For Output:
    mov ah,2
    mov dl,bl
    int 21h

## Slide 8
  Return

## Slide 10
Experiment No: 01
Name of the Experiment:
    Write an assembly language program for simple input and output using EMU8086.
    Write an assembly language program for simple input and output, where the output is displayed on a new line using EMU8086.

## Slide 11
  Write an assembly language program for simple input and output using EMU8086.

## Slide 12
ii. Write an assembly language program for simple input and output, where the output is displayed on a new line using EMU8086.