## Slide 1: ALU Design Example (1-bit & 4-bit)
Protik Chakroborty Lecturer CSE, VU

## Slide 2: ALU in CPU
Control Unit (CU)
Register File
RAM
(Main
Memory)
Program Counter (PC)
Arithmetic and Logic Unit (ALU)
op [1]
op [0]
+1
d [0]
Ra Rb
Wr Wrd
a
b
a
b
clk
r
d [3]
a[1] d [2]
a[0] d [1]
Program Counter will have address of next instruction to be executed in current clock cycle.
Address in PC will be sent to RAM to retrieve instruction.
Instruction will be decoded by control unit and will select registers and/or immediate values.
Data within registers and/or immediate values will be sent to Arithmetic and Logic Unit (ALU) to perform operations.
The ALU will perform operation and result will be sent to the register to be written.
Finally, PC will be incremented to point to the next instruction in next clock cycle.
i[1] o[1]
i[0] o[0]
PC
op_sel[1] op_sel[0]
alu[1]alu[0]
Figure: 1-bit CPU
ADD R1, R0

## Slide 3: ALU in CPU
Program Counter will have address of next instruction to be executed in current clock cycle.
Address in PC will be sent to RAM to retrieve instruction.
Instruction will be decoded by control unit and will select registers and/or immediate values.
Data within registers and/or immediate values will be sent to Arithmetic and Logic Unit (ALU) to perform operations.
The ALU will perform operation and result will be sent to the register to be written.
Finally, PC will be incremented to point to the next instruction in next clock cycle.
Figure: 1-bit CPU
Control Unit (CU)
Register File
RAM
(Main
Memory)
Program Counter (PC)
op [1]
op [0]
+1
d [0]
Ra Rb
Wr
Wrd
a
b
a
clk
alu[1]
r
d [3]
a[1] d [2]
a[0] d [1]
i[1] o[1]
i[0] o[0]
PC
op_sel[1] op_sel[0]
alu[0]
Arithmetic
and Logic
UnSit (ALU)
b

## Slide 4: ALU Basics

## Slide 5: ALU
Arithmetic Logic Unit (ALU) is a combinational digital circuit that performs arithmetic and bitwise operations on integer binary numbers. It is a fundamental building block of Central Processing Unit (CPU) of computers.
The inputs to an ALU are the data to be operated on, called operands, and a code indicating the operation to be performed. The ALU's output is the result of the performed operation.
In many designs, the ALU also has status/FLAG inputs or outputs, or both, which convey information about a previous operation or the current operation, respectively, between the ALU and external status/FLAG registers.

## Slide 6: Functions of ALU
a. Arithmetic operations:
Add: A and B are summed and the sum appears at Y and carry-out.
Add with carry: A, B and carry-in are summed and the sum appears at Y
and carry-out.
Subtract: B is subtracted from A (or vice versa) and the difference appears at Y and carry-out. For this function, carry-out is effectively a "borrow" indicator. This operation may also be used to compare the magnitudes of A and B; in such cases the Y output may be ignored by the processor, which is only interested in the status bits (particularly zero and negative) that result from the operation.
Subtract with borrow: B is subtracted from A (or vice versa) with borrow (carry-in) and the difference appears at Y and carry-out (borrow out).
Two's complement (negate): A (or B) is subtracted from zero and the difference appears at Y.
Increment: A (or B) is increased by one and the resulting value appears at Y.
Decrement: A (or B) is decreased by one and the resulting value appears at Y.

## Slide 7: Functions of ALU
Bitwise logical operations:
  AND: the bitwise AND of A and B appears at Y.
  OR: the bitwise OR of A and B appears at Y.
  Exclusive-OR: the bitwise XOR of A and B appears at Y.
  Ones' complement: all bits of A (or B) are inverted and appear at Y.
Bit shift operations: ALU shift operations cause operand A (or B) to shift left or right (depending on the opcode) and the shifted operand appears at Y.
  Arithmetic shift: The operand is treated as a two's complement integer,
meaning that the most significant bit is a "sign" bit and is preserved.
  Logical shift: A logic zero is shifted into the operand. This is used to shift unsigned integers.
  Rotate: The operand is treated as a circular buffer of bits so its least and most significant bits are effectively adjacent.
  Rotate through carry: The carry bit and operand are collectively treated as a circular buffer of bits.

## Slide 8: Functions of ALU

## Slide 9: FPU
A floating-point unit (FPU, colloquially a math coprocessor) is a part of a computer system specially designed to carry out operations on floating-point numbers. Typical operations are addition, subtraction, multiplication, division, and square root.
In general-purpose computer architectures, one or more FPUs may be integrated as execution units within the Central Processing Unit (CPU). However, many embedded processors/microcontrollers do not have hardware support for floating-point operations.
When a CPU is executing a program that calls for a floating-point operation, there are three ways to carry it out:
A floating-point unit emulator (A floating-point library/Software).
Add-on FPU (Coprocessor/Not inside Processor).
Integrated FPU (Inside Processor).

## Slide 10: Example 1: 1-bit ALU design
𝑺𝟏

## Slide 11: 1-bit AND gate
𝐀
𝐁
𝐀𝐁
A
B
AND
O

## Slide 12: 1-bit OR gate
𝐀 + 𝐁
𝐀
𝐁
A
B
OR
O

## Slide 13: 1-bit XOR gate
𝐀⨁𝐁
𝐀
𝐁
A
B
XOR
O

## Slide 14: 1-bit Adder
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
 B
Cout  A B  A C C
S  A B Cin A B Cin A B Cin  A B Cin
FA
A
B
Cin
Cout
S

## Slide 15: 1-bit Subtractor
FA
S
C
A
B
Cin =1
B
FA
A
B
Cin
Cout
S
Cin=1

## Slide 16: 1-bit Adder (Modified)
FA
S
C
A
B
B
Cin=0
Cin=0

## Slide 17: 1-bit Adder/Subtractor
FA
S
A
B
B
Cin/Sel
A B
Sel
ADD/SUB
S

## Slide 18: 1-bit Multiplier
𝐀
𝐁
𝐀𝐁
𝟎 ∗ 𝟎 = 𝟎
𝟎 ∗ 𝟏 = 𝟎
𝟏 ∗ 𝟎 = 𝟎
𝟏 ∗ 𝟏 = 𝟏
𝐀
𝐁 𝐌
A
B
MUL
O

## Slide 19: 1-bit Shifter
𝐘 = 𝐀ഥ. 𝐁ഥ. 𝐃𝟎 + 𝐀ഥ. 𝐁. 𝐃𝟏 + 𝐀. 𝐁ഥ. 𝐃𝟐 + 𝐀. 𝐁. 𝐃𝟑

## Slide 20: 1-bit Shifter
𝑺𝟏 | 𝑺𝟐 | Output | Operation
0 | 0 | A | No Shift
0 | 1 | 0 | Left Shift
1 | 0 | 0 | Right Shift
1 | 1 | X | X
Input: A
Right shift: 0A Left shift: A0
Input: 1
Right shift: 01
Left shift: 10
A
0 0
X
O
𝟑 𝟐 𝟏 𝟎
4 to 1 MUX

## Slide 21: 1-bit Shifter A
𝑺𝟏 | 𝑺𝟐 | Output | Operation
0 | 0 | A | No Shift
0 | 1 | 0 | Left Shift
1 | 0 | 0 | Right Shift
1 | 1 | X | X
SHIFT
O
A
𝑺𝟏
𝑺𝟐
0 0
X
O
𝟑 𝟐 𝟏 𝟎
4 to 1 MUX

## Slide 22: All the circuits so far
A B
AND
O
A B
OR
O
A B
XOR
O
ADD/SUB
S
A B
Sel
A B
MUL
O
SHIFT
O
A
𝐒𝟐
𝐒𝟏
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓

## Slide 23: ALU Circuit
S
A
O
B
S

## Slide 24: 1-bit CPU
S
Control Unit (CU)
Register File
RAM
(Main
Memory)
Program Counter (PC)
op [1]
op [0]
+1
d [3]
a[1]
d [0]
Ra Rb
Wr Wrd
a
b
a
clk
alu[1]
r
d [2]
a[0] d [1]
i[1] o[1]
i[0] o[0]
PC
op_sel[1] op_sel[0]
alu[0]
Arithmetic and Logic Unit (ALU)
b
Figure: 1-bit CPU

## Slide 25: ALU Circuit
Available Operations: ADD,
SUB, MUL, AND, OR, XOR,
LEFT SHIFT, RIGHT SHIFT
All operations will
be executed at the same.
Only one operation must be selected by Control Unit.
Total Operations: 8
A
B
R
S
S

## Slide 26: 1-bit ALU Circuit
Available Operations: ADD,
SUB, MUL, AND, OR, XOR,
LEFT SHIFT, RIGHT SHIFT
Total Operations: 8
So, selection line must support at least 8 combinations.
A
B
R
S
𝐒𝟐
𝐒𝟏
𝐒𝟎

## Slide 27: 1-bit ALU Circuit
We will need a MUX to select our expected output.
As there are eight operations in total, we will use 8 to 1 MUX
A
B
S
R
𝐒𝟐
𝐒𝟏
𝐒𝟎

## Slide 28: 1-bit ALU Circuit 8 to 1 MUX
𝐒𝟐 | 𝐒𝟏 | 𝐒𝟎 | 𝐘
0 | 0 | 0 | 𝐈𝟎
0 | 0 | 1 | 𝐈𝟏
0 | 1 | 0 | 𝐈𝟐
0 | 1 | 1 | 𝐈𝟑
1 | 0 | 0 | 𝐈𝟒
1 | 0 | 1 | 𝐈𝟓
1 | 1 | 0 | 𝐈𝟔
1 | 1 | 1 | 𝐈𝟕
𝐘 = 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟎 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟏 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟐 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟑 +
𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟒 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟓 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟔 + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟕
0
1
2
3
4
5
6
7
𝐈𝟎
Y
𝐈𝟏
𝐈𝟐
𝐈𝟑
𝐈𝟒
𝐈𝟓
𝐈𝟔
𝐈𝟕
𝐒𝟐 𝐒𝟏 𝐒𝟎

## Slide 29: 1-bit ALU Circuit
Operation | 𝐒𝟐 | 𝐒𝟏 | 𝐒𝟎 | 𝐎
AND | 0 | 0 | 0 | 𝐈𝟎
OR | 0 | 0 | 1 | 𝐈𝟏
XOR | 0 | 1 | 0 | 𝐈𝟐
LEFT SHIFT | 0 | 1 | 1 | 𝐈𝟑
RIGHT SHIFT | 1 | 0 | 0 | 𝐈𝟒
ADD | 1 | 0 | 1 | 𝐈𝟓
SUB | 1 | 1 | 0 | 𝐈𝟔
MUL | 1 | 1 | 1 | 𝐈𝟕
0
1
2
3
4
5
6
7
𝐈𝟎
Y
𝐈𝟏
𝐈𝟐
𝐈𝟑
𝐈𝟒
𝐈𝟓
𝐈𝟔
𝐈𝟕
𝐒𝟐 𝐒𝟏 𝐒𝟎
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓

## Slide 30: 1-bit ALU Circuit
Operation | 𝐒𝟐 | 𝐒𝟏 | 𝐒𝟎 | 𝐎
AND | 0 | 0 | 0 | 𝐈𝟎
OR | 0 | 0 | 1 | 𝐈𝟏
XOR | 0 | 1 | 0 | 𝐈𝟐
LEFT SHIFT | 0 | 1 | 1 | 𝐈𝟑
RIGHT SHIFT | 1 | 0 | 0 | 𝐈𝟒
ADD | 1 | 0 | 1 | 𝐈𝟓
SUB | 1 | 1 | 0 | 𝐈𝟔
MUL | 1 | 1 | 1 | 𝐈𝟕
0
1
2
3
4
5
6
7
𝐈𝟎
Y
𝐈𝟏
𝐈𝟐
𝐈𝟑
𝐈𝟒
𝐈𝟓
𝐈𝟔
𝐈𝟕
𝐒𝟐 𝐒𝟏 𝐒𝟎
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓

## Slide 31: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
0 0 0
𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
A B

## Slide 32: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
A B
0 0 1
0 1 0

## Slide 33: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
𝑺𝟏 SHIFT
𝑺𝟎
A B
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓
0 1
1
0
1 0

## Slide 34: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
𝑺𝟏 SHIFT
𝑺𝟎
A B
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓
0 1
1
0
1 0

## Slide 35: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
A B
ADD/SUB
𝑺𝒆𝒍
1 0 1
1 1 0
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁

## Slide 36: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
A B
ADD/SUB
𝑺𝒆𝒍
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
1 0 1
1 1 0

## Slide 37: 1-bit ALU Circuit
0
1
2
3
4
5
6
7
R
𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
𝑺𝟏 SHIFT
𝑺𝟎
MUL
A B
ADD/SUB
𝑺𝒆𝒍

## Slide 38: Example 2: 4-bit ALU design

## Slide 39: 4-bit AND gate
A[3:0]
B[3:0]
AND
O[3:0]
𝐀[𝟑]
𝐁[𝟑]
𝟎[𝟑]
𝐀[𝟐]
𝐁[𝟐]
𝐀[𝟏]
𝟎[𝟐]
𝐁[𝟏]
𝐀[𝟎]
𝟎[𝟏]
𝐁[𝟎]
𝟎[𝟎]

## Slide 40: 4-bit OR gate
A[3:0]
B[3:0]
OR
O[3:0]
𝐀[𝟑]
𝐁[𝟏]
𝐀[𝟎]
𝟎[𝟏]
𝐁[𝟎]
𝟎[𝟎]
𝐁[𝟐]
𝐀[𝟏]
𝐁[𝟑]
𝐀[𝟐]
𝟎[𝟐]
𝟎[𝟑]

## Slide 41: 4-bit OR gate
A[3:0]
B[3:0]
XOR
O[3:0]
𝐀[𝟏]
𝐁[𝟏]
𝐀[𝟎]
𝟎[𝟏]
𝐁[𝟎]
𝟎[𝟎]
𝐀[𝟑]
𝐁[𝟑]
𝟎[𝟑]
𝐀[𝟐]
𝐁[𝟐]
𝟎[𝟐]

## Slide 42: 2-bit Adder/Subtractor
A[3:0]
B[3:0]
Sel
ADD/SUB
S[3:0]
FA
S[0]
A[0]
Cin/Sel
FA
B[1] B[0]
S[1]
A[1]
FA
S[2]
A[0]
B[0]
FA
S[3]
B[1]
A[1]

## Slide 43: 4-bit Unsigned Multiplier
𝐀𝟏
𝐁𝟏
𝐀𝟎
𝐁𝟎
 | 𝐀𝟏𝐁𝟏 | 𝐀𝟏𝐁𝟎 𝐀𝟎𝐁𝟏 | 𝐀𝟎𝐁𝟎
𝐌𝟑 | 𝐌𝟐 | 𝐌𝟏 | 𝐌𝟎
A[0]
HA
M[0]
B[0]
A[1]
B[1]
A[0]
A[1]
FA
M[1]
M[2]
M[3]

## Slide 44: 4-bit Unsigned Multiplier
A[1:0]
B[1:0]
MUL
S[3:0]
A[0]
HA
M[0]
B[0]
A[1]
B[1]
A[0]
A[1]
FA
M[1]
M[2]
M[3]

## Slide 45: 4-bit Shifter
𝑺𝟏 | 𝑺𝟐 | Output | Operation
0 | 0 | A[3]A[2]A[1]A[0] | No Shift
0 | 1 | A[2]A[1]A[0] 0 | Left Shift
1 | 0 | 0 A[3]A[2]A[1] | Right Shift
1 | 1 | X | X
Input: A[3]A[2]A[1]A[0]
Right shift: 0 A[3]A[2]A[1] Left shift: A[2]A[1]A[0] 0
A[0]
O[0]
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
A[1]
A[0] 0
X A[2] X A[1]
O[1]
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
O[2]
𝟑 𝟐 𝟏 𝟎
4 to 1 MUX
0
X
O[3]
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
A[2]
A[1]
X A[3]
A[3]
A[2]

## Slide 46: 4-bit Shifter
A[0]
O
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
A[1]
A[0] 0
X A[2] X A[1]
O
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
O
𝟑 𝟐 𝟏 𝟎
4 to 1 MUX
0
X
O
𝟑 𝟐 𝟏 𝟎
4 to 1
MUX
A[2]
A[1]
X A[3]
A[3]
A[2]
SHIFT
O[3:0]
A[3:0]
S[1]
S[0]

## Slide 47: All the circuits so far
A[3:0]
B[3:0]
Sel
ADD/SUB
S[3:0]
A[1:0]
B[1:0]
MUL
O[3:0]
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓
A[3:0]
AND
O[3:0]
B[3:0]
A[3:0]
OR
O[3:0]
B[3:0]
A[3:0]
XOR
O[3:0]
B[3:0]
A[3:0]
S[1]
S[0]
SHIFT
O[3:0]

## Slide 48: 4-bit ALU Circuit
S[2:0]
A[3:0]
O[3:0]
B[3:0]
S

## Slide 49: 4-bit ALU Circuit 8 to 1 MUX
0
1
2
3
4
5
6
7
𝐈𝟎
Y
𝐈𝟏
𝐈𝟐
𝐈𝟑
𝐈𝟒
𝐈𝟓
𝐈𝟔
𝐈𝟕
𝐒𝟐 𝐒𝟏 𝐒𝟎
But this MUX can handle only 1 bit. How can we build 4-bit MUX?

## Slide 50: 4-bit ALU Circuit 8 to 1 MUX
0
1
2
3
4
5
6
7
𝐈𝟎
Y
𝐈𝟏
𝐈𝟐
𝐈𝟑
𝐈𝟒
𝐈𝟓
𝐈𝟔
𝐈𝟕
𝐒𝟐 𝐒𝟏 𝐒𝟎
But this MUX can handle only 1 bit. How can we build 4-bit MUX?
Solution is to use FOUR 8 to 1 MUX for 4 input lines and 4 output lines.

## Slide 51: 4-bit ALU Circuit 4-bit 8 to 1 MUX
Y[3]
5
6
7
𝐈𝟎[𝟑] 𝐈𝟏[𝟑] | 0 1
𝐈𝟐[𝟑] | 2
𝐈𝟑[𝟑] | 3
𝐈𝟒[𝟑] | 4
𝐈𝟓[𝟑] | 5
𝐈𝟔[𝟑] | 6
𝐈𝟕[𝟑] | 7
𝐈𝟎[𝟐] | 0
𝐈𝟏[𝟐] | 1
𝐈𝟐[𝟐] | 2
𝐈𝟑[𝟐] | 3
𝐈𝟒[𝟐] | 4
Y[2]
𝐈𝟓[𝟐]
𝐈𝟔[𝟐]
𝐈𝟕[𝟐]
0
1
2
3
4
5
6
7
𝐈𝟎[𝟏]
𝐈𝟏[𝟏]
𝐈𝟐[𝟏]
𝐈𝟑[𝟏]
𝐈𝟒[𝟏]
𝐈𝟓[𝟏]
𝐈𝟔[𝟏]
𝐈𝟕[𝟏]
Y[1]
S[2:0]
0
1
2
3
4
5
6
7
𝐈 [𝟎]
𝟎
𝐈𝟏[𝟎]
𝐈𝟐[𝟎]
𝐈𝟑[𝟎]
𝐈𝟒[𝟎]
𝐈𝟓[𝟎]
𝐈𝟔[𝟎]
𝐈𝟕[𝟎]
Y[0]
3
3
3
3
3

## Slide 52: 4-bit ALU Circuit 8 to 1 MUX
0
1
2
3
4
5
6
7
𝐈𝟎[3:0]
Y[3:0]
𝐈𝟏[3:0]
𝐈𝟐[3:0]
𝐈𝟑[3:0]
𝐈𝟒[3:0]
𝐈𝟓[3:0]
𝐈𝟔[3:0]
𝐈𝟕[3:0]
𝐒𝟐 𝐒𝟏 𝐒𝟎
𝐒𝟐 | 𝐒𝟏 | 𝐒𝟎 | 𝐘[3] | 𝐘[2] | 𝐘[1] | 𝐘[0]
0 | 0 | 0 | 𝐈𝟎[3] | 𝐈𝟎[2] | 𝐈𝟎[1] | 𝐈𝟎[0]
0 | 0 | 1 | 𝐈𝟏[3] | 𝐈𝟏[2] | 𝐈𝟏[1] | 𝐈𝟏[0]
0 | 1 | 0 | 𝐈𝟐[3] | 𝐈𝟐[2] | 𝐈𝟐[1] | 𝐈𝟐[0]
0 | 1 | 1 | 𝐈𝟑[3] | 𝐈𝟑[2] | 𝐈𝟑[1] | 𝐈𝟑[0]
1 | 0 | 0 | 𝐈𝟒[3] | 𝐈𝟒[2] | 𝐈𝟒[1] | 𝐈𝟒[0]
1 | 0 | 1 | 𝐈𝟓[3] | 𝐈𝟓[2] | 𝐈𝟓[1] | 𝐈𝟓[0]
1 | 1 | 0 | 𝐈𝟔[3] | 𝐈𝟔[2] | 𝐈𝟔[1] | 𝐈𝟔[0]
1 | 1 | 1 | 𝐈𝟕[3] | 𝐈𝟕[2] | 𝐈𝟕[1] | 𝐈𝟕[0]
𝐘[𝟑] = 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟎[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟏[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟐[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟑[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟒[𝟑] +
𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟓[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟔[𝟑] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟕[𝟑]
𝐘[𝟐] = 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟎[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟏[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟐[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟑[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟒[𝟐] +
𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟓[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟔[𝟐] + 𝐒𝟐. 𝐒𝟏. 𝐒𝟎. 𝐈𝟕[𝟐]

## Slide 53: 4-bit ALU Circuit
Operation | 𝐒𝟐 | 𝐒𝟏 | 𝐒𝟎 | 𝐘[3] | 𝐘[2] | 𝐘[1] | 𝐘[0]
AND | 0 | 0 | 0 | 𝐈𝟎[3] | 𝐈𝟎[2] | 𝐈𝟎[1] | 𝐈𝟎[0]
OR | 0 | 0 | 1 | 𝐈𝟏[3] | 𝐈𝟏[2] | 𝐈𝟏[1] | 𝐈𝟏[0]
XOR | 0 | 1 | 0 | 𝐈𝟐[3] | 𝐈𝟐[2] | 𝐈𝟐[1] | 𝐈𝟐[0]
LEFT SHIFT | 0 | 1 | 1 | 𝐈𝟑[3] | 𝐈𝟑[2] | 𝐈𝟑[1] | 𝐈𝟑[0]
RIGHT SHIFT | 1 | 0 | 0 | 𝐈𝟒[3] | 𝐈𝟒[2] | 𝐈𝟒[1] | 𝐈𝟒[0]
ADD | 1 | 0 | 1 | 𝐈𝟓[3] | 𝐈𝟓[2] | 𝐈𝟓[1] | 𝐈𝟓[0]
SUB | 1 | 1 | 0 | 𝐈𝟔[3] | 𝐈𝟔[2] | 𝐈𝟔[1] | 𝐈𝟔[0]
MUL | 1 | 1 | 1 | 𝐈𝟕[3] | 𝐈𝟕[2] | 𝐈𝟕[1] | 𝐈𝟕[0]
If 𝐬𝐞𝐥 = 𝟎, 𝐒 = 𝐀𝐃𝐃
If 𝐬𝐞𝐥 = 𝟏, 𝐒 = 𝐒𝐔𝐁
If 𝐒𝟏 = 𝟎, 𝐒𝟎 = 𝟏, 𝐒 = 𝐋𝐄𝐅𝐓 𝐒𝐇𝐈𝐅𝐓
If 𝐒𝟏 = 𝟏, 𝐒𝟎 = 𝟎, 𝐒 = 𝐑𝐈𝐆𝐇𝐓 𝐒𝐇𝐈𝐅𝐓
0
1
2
3
4
5
6
7
𝐈𝟎[3:0]
Y[3:0]
𝐈𝟏[3:0]
𝐈𝟐[3:0]
𝐈𝟑[3:0]
𝐈𝟒[3:0]
𝐈𝟓[3:0]
𝐈𝟔[3:0]
𝐈𝟕[3:0]
𝐒𝟐 𝐒𝟏 𝐒𝟎

## Slide 54: 4-bit ALU Circuit
0
1
2
3
4
5
6
7
R[3:0]
𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
𝑺𝟏 SHIFT
𝑺𝟎
MUL
A[3:0] B[3:0]
ADD/SUB
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
A[1:0]
2
B[1:0]

## Slide 55
4-bit 8 to 1 MUX
0
1
2
3
4
5
6
7
𝐈𝟎[𝟑]
Y[3]
𝐈𝟏[𝟑]
𝐈𝟐[𝟑]
𝐈𝟑[𝟑]
𝐈𝟒[𝟑]
𝐈𝟓[𝟑]
𝐈𝟔[𝟑]
𝐈𝟕[𝟑]
0
1
2
3
4
5
6
7
Y[2]
𝐈𝟏[𝟐]
𝐈𝟐[𝟐]
𝐈𝟑[𝟐]
𝐈𝟒[𝟐]
𝐈𝟓[𝟐]
𝐈𝟔[𝟐]
𝐈𝟕[𝟐]
0
1
2
3
4
5
6
7
𝐈𝟎[𝟏]
Y[1]
𝐈𝟏[𝟏]
𝐈𝟐[𝟏]
𝐈𝟑[𝟏]
𝐈𝟒[𝟏]
𝐈𝟓[𝟏]
𝐈𝟔[𝟏]
𝐈𝟕[𝟏]
S[2:0]
0
1
2
3
4
5
6
7
𝐈𝟎[𝟎]
Y[0]
𝐈 [𝟎]
𝟏
𝐈𝟐[𝟎]
𝐈𝟑[𝟎]
𝐈𝟒[𝟎]
𝐈𝟓[𝟎]
𝐈𝟔[𝟎]
𝐈𝟕[𝟎]
3 𝐈𝟎[𝟐]
3
3
For AND operation 4-bit 8 to 1 MUX will be like
A[3:0] B[3:0]
AND
O[3:0]
3
O[3]
O[2]
O[1]
O[0]
3

## Slide 56
Home Work:
Design a 2-bit ALU that supports following operations: AND, LEFT SHIFT, MUL & SUB.

## Slide 57: Calculating FLAG Values in ALU

## Slide 58: Question: How can we implement conditional branch instructions like JE, JNE, JG, JL, JLE etc.?
Answer:
We can implement conditional instructions by using FLAG values. Flag values are stored in FLAG Register.

## Slide 59: FLAG Register
FLAG register always save state of previous instruction. Its flags will be on/off depending on result of previous instruction.
We learned about 8 flags in 8086 processor. They are:
Sign Flag Zero Flag
Auxiliary Cary Flag
Parity Flag Carry Flag Overflow Flag Directional Flag Interrupt Flag Trap Flag

## Slide 60: FLAG Register
We will implement 3 flags in our CPU. They are:
Carry Flag (CF): It will be ON/1 when result of ADD/SUB have carry.
Sign Flag (SF): It will determine whether result is positive or negative.
Zero Flag (ZF): It will determine whether result is 0.
Flag value depends on Result of ALU.

## Slide 61: 4 bit ALU
cf
LEFT ROTATE
S[1:0]
2
NOT
4
4
4
0 0 0 0 (0)
0 0 0 1 (1)
0 0 1 0 (2)
0 0 1 1 (3)
0 1 0 0 (4)
0 1 0 1 (5)
0 1 1 0 (6)
0 1 1 1 (7)
1 0 0 0 (8)
1 0 0 1 (9)
1 0 1 0 (10)
1 0 1 1 (11)
1 1 0 0 (12)
1 1 0 1 (13)
1 1 1 0 (14)
1 1 1 1 (15)
R[3:0]
𝐒𝟑 𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
ADD/SUB
LEFT SHIFT
S[1:0]
MUL
A[3:0] B[3:0]
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
2
A[1:0]
B[1:0]
RIGHT SHIFT
S[1:0]
RIGHT ROTATE
S[1:0]
4
4
4
DIV
2
4
4
4
CMP (SUB)
4
2
2
4
B[1:0]
B[1:0]
B[1:0]
B[1:0]
C
1
Carry Flag (CF) is already implemented.

## Slide 62: 4 bit ALU
cf
LEFT ROTATE
S[1:0]
2
NOT
4
4
4
0 0 0 0 (0)
0 0 0 1 (1)
0 0 1 0 (2)
0 0 1 1 (3)
0 1 0 0 (4)
0 1 0 1 (5)
0 1 1 0 (6)
0 1 1 1 (7)
1 0 0 0 (8)
1 0 0 1 (9)
1 0 1 0 (10)
1 0 1 1 (11)
1 1 0 0 (12)
1 1 0 1 (13)
1 1 1 0 (14)
1 1 1 1 (15)
R[3:0]
𝐒𝟑 𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
ADD/SUB
LEFT SHIFT
S[1:0]
MUL
A[3:0] B[3:0]
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
2
A[1:0]
B[1:0]
RIGHT SHIFT
S[1:0]
RIGHT ROTATE
S[1:0]
4
4
4
DIV
2
4
4
4
CMP (SUB)
4
2
2
4
B[1:0]
B[1:0]
B[1:0]
B[1:0]
C
1
How about Sign Flag?
MSB bit of result determine whether number is positive or negative.

## Slide 63: 4 bit ALU
sf
cf
LEFT ROTATE
S[1:0]
2
NOT
4
4
4
0 0 0 0 (0)
0 0 0 1 (1)
0 0 1 0 (2)
0 0 1 1 (3)
0 1 0 0 (4)
0 1 0 1 (5)
0 1 1 0 (6)
0 1 1 1 (7)
1 0 0 0 (8)
1 0 0 1 (9)
1 0 1 0 (10)
1 0 1 1 (11)
1 1 0 0 (12)
1 1 0 1 (13)
1 1 1 0 (14)
1 1 1 1 (15)
R[3:0]
𝐒𝟑 𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
ADD/SUB
LEFT SHIFT
S[1:0]
MUL
A[3:0] B[3:0]
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
2
A[1:0]
B[1:0]
RIGHT SHIFT
S[1:0]
RIGHT ROTATE
S[1:0]
4
4
4
DIV
2
4
4
4
CMP (SUB)
4
2
2
4
B[1:0]
B[1:0]
B[1:0]
B[1:0]
C
1
How about Zero Flag?
If all the bits of R is NORed together, then Zero Flag value will be 1 only if all the bits of R is 0.

## Slide 64: FLAG Register Implementation
LEFT ROTATE
S[1:0]
2
NOT
4
4
4
0 | 0 | 0 | 0 (0)
0 | 0 | 0 | 1 (1)
0 | 0 | 1 | 0 (2)
0 | 0 | 1 | 1 (3)
0 | 1 | 0 | 0 (4)
0 | 1 | 0 | 1 (5)
0 | 1 | 1 | 0 (6)
0 | 1 | 1 | 1 (7)
1 | 0 | 0 | 0 (8)
1 | 0 | 0 | 1 (9)
1 | 0 | 1 | 0 (10)
1 | 0 | 1 | 1 (11)
1 | 1 | 0 | 0 (12)
1 | 1 | 0 | 1 (13)
1 | 1 | 1 | 0 (14)
1 | 1 | 1 | 1 (15)
R[3:0]
𝐒𝟑 𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
ADD/SUB
LEFT SHIFT
S[1:0]
MUL
A[3:0] B[3:0]
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
2
A[1:0]
B[1:0]
RIGHT SHIFT
S[1:0]
RIGHT ROTATE
S[1:0]
4
4
4
DIV
2
4
4
4
CMP (SUB)
4
2
2
4
B[1:0]
B[1:0]
B[1:0]
B[1:0]
C
1
sf
cf
R[3]
R[2]
R[1]
R[0]
We need to store these flags in a
3-bit FLAG Register.
zf

## Slide 65: 4 bit ALU
cf
LEFT ROTATE
S[1:0]
2
NOT
4
4
4
0 0 0 0 (0)
0 0 0 1 (1)
0 0 1 0 (2)
0 0 1 1 (3)
0 1 0 0 (4)
0 1 0 1 (5)
0 1 1 0 (6)
0 1 1 1 (7)
1 0 0 0 (8)
1 0 0 1 (9)
1 0 1 0 (10)
1 0 1 1 (11)
1 1 0 0 (12)
1 1 0 1 (13)
1 1 1 0 (14)
1 1 1 1 (15)
R[3:0]
𝐒𝟑 𝐒𝟐 𝐒𝟏 𝐒𝟎
AND
OR
XOR
ADD/SUB
LEFT SHIFT
S[1:0]
MUL
A[3:0] B[3:0]
𝑺𝒆𝒍
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
4
2
2
A[1:0]
B[1:0]
RIGHT SHIFT
S[1:0]
RIGHT ROTATE
S[1:0]
4
4
4
DIV
2
4
4
4
CMP (SUB)
4
2
2
4
B[1:0]
B[1:0]
B[1:0]
B[1:0]
C
1
sf
R[3]
R[2]
R[1]
R[0]
zf
dzf
dsf
dcf
clk
3 bit FLAG Register
(without selection line)

## Slide 66: Example: ALU
Question: Design a 4-bit ALU that supports RIGHT ROTATE and DIV (Unsigned) operations.
Answer:
4-bit RIGHT ROTATE Circuit:
Figure: 4-bit RIGHT
ROTATE Chip
Figure: 4-bit RIGHT ROTATE Circuit
1 bit 4-to-1 MUX

## Slide 67: Example: ALU
4-bit DIV (Unsigned) Circuit:
Figure: 1-bit Full Adder
Chip
Figure: 1-bit Full Adder Circuit

## Slide 68: Example: ALU
4-bit DIV (Unsigned) Circuit:
Figure: Cell M (Divider Block) Chip
Figure: Cell M (Divider Block)

## Slide 69: Example: ALU
4-bit DIV (Unsigned) Circuit:
Figure: 4-bit Unsigned Divider

## Slide 70: Example: ALU
4-bit DIV (Unsigned) Circuit:
Figure: 4-bit Unsigned Divider Chip

## Slide 71: Example: ALU
4-bit ALU Circuit:
Figure: 4-bit ALU Circuit that supports RIGHT ROTATE and DIV
Figure: 4-bit ALU Circuit Chip
4 bit 2-to-1 MUX

## Slide 72: Exercises
Draw/Design/Implement an 1-bit/2-bit/3-bit/4-bit/5-bit ALU that supports following operations:
  ADD /
  SUB /
  MUL /
  DIV /
  LEFT SHIFT /
  RIGHT SHIFT /
  LEFT ROTATE /
  RIGHT ROTATE /
  AND /
  OR /
  XOR /
  NOT / xiii.CMP

## Slide 73: Thank You 